## Slide 1: A basic overview of Proteomics
Bioinformatics Unit Lab Meeting
F.M. Mancuso
21/02/2012

## Slide 2
The proteome is defined as the set of all expressed proteins in a cell, tissue or organism (Wilkins et al., 1997).
Proteomics can be defined as the systematic analysis of proteins for their identity, quantity and function.
Protein alterations cannot be fully deduced from DNA.
RNA expression does not always reflect protein levels (i.e. translational control, degradation, turnover,…)
Some tissues not suitable for RNA expression analysis.
Proteins are the physiological/pathological active key players.
General goal:
  better understanding of genesis and progression of diseases
Clinical goals:
  early disease detection (biomarkers)
  identification of therapeutic targets
  therapy monitoring
Why proteomics?

## Slide 3: Applications of Proteomics
Mining: identification of proteins (catalog the proteins)
Quantitative proteomics: defining the relative or absolute amount of a protein
Protein-expression profile: identification of proteins in a particular state of the organism
Protein-network mapping: protein interactions in living systems
Mapping of protein modifications: how and where proteins are modified.

## Slide 4: Top down or bottom up?
Bottom-up
  Most common
  Starting with proteolytic fragments
  Piecing the protein back together
    de novo repeat detection
Top down
  Tandem MS of whole protein ions
    Pulling them apart
  Electron capture dissociation
  Extensive sequence information
Fragment ions of peptides
MS/MS
Proteolytic digest
e.g. Trypsin
Protein
MS/MS
Fragment ions of protein
Bottom-up
Top down
”Protein mass spectrometry" Wikipedia, The Free Encyclopedia. Wikimedia Foundation, Inc.

## Slide 5: Typical MS experiment (I)
Protein Identification (and quantitation)

## Slide 6
Sample preparation
Separation
Ionisation
Identification
Quantification
Bioinformatics
Bioanalytics
TOF, Q, IT
MALDI, ESI
HPLC
Cells, tissue
Algorithms
Typical MS experiment (II)
Notes: Sample preparation: cells, body fluids, tissues
Chromatography electrophoresis
• different combinations: accuracy, sensitivity, mass range …
secondary electron multiplier
micro channel plates
time-of-flight (TOF)
quadrupol (Q)
ion trap (IT)
fourier transform ion cyclotron (FTICR)

## Slide 7: Mass Spectrometry (MS) Stages
Introduce sample to the instrument
Generate ions in the gas phase
Separate ions on the basis of differences in m/z with a mass analyzer
Detect ions
Vacuum System
Samples
HPLC
Detector
Data System
Mass Analyser
Ionisation Method
MALDI
ESI

## Slide 8
Aebersold R. and Mann M., Nature (2003)
Mass spectrometers used in proteomic research

## Slide 9
0
20
40
60
80
100
120
140
160
180
200
Time (min)
0
10
20
30
40
50
60
70
80
90
100
0
10
20
30
40
50
60
70
80
90
100
47.64
75.81
57.90
82.90
104.24
111.77
74.48
134.78
46.01
3.39
26.43
140.20
146.61
206.18
160.29
181.98
47.97
83.07
82.07
70.11
85.56
102.41
126.89
46.01
134.78
43.63
29.48
144.13
172.59
163.97
27.29
19.24
181.98
197.48
NL: 2.83E9
TIC MS
RS_Contest_04
NL: 4.22E8
Base Peak m/z=
400.0-2000.0 F: + c
Full ms [
400.00-2000.00]
MS RS_Contest_04
Data acquired - Chromatogram

## Slide 11: Tandem mass spectrum

## Slide 12: Tandem mass spectra (MS/MS) can be used for peptide sequencing
- Database Searching
- De novo sequencing

## Slide 13: Mascot
  Scoring based on peptide frequency distribution from a non-redundant database (MOWSE – Molecular Weight SEarch)
  The significance of that result depends on the size of the database being searched. Mascot shades in green the insignificant hits using a P=0.05 cutoff.

## Slide 17: Quantitative Proteomics
Kumar et al., FEBS Letters (2009)

## Slide 18: Relative quantitation methods
i.e. SILAC
i.e. ICAT
i.e. iTRAQ,
TMT

## Slide 19
Yates JR, et al. Annu Rev Biomed Eng. (2009)
Isotopic labeling
Label-free analysis
Quantitation methods (II)

## Slide 20: Quantitation methods (III)

## Slide 21
Boxes in blue and yellow represent two experimental conditions. Horizontal lines indicate when samples are combined.
Dashed lines indicate points at which experimental variation and thus quantification errors can occur.
Bantscheff et al., Anal Bioanal Chem (2007)
Common quantitative MS workflows

## Slide 22
Yellow icons indicate steps common to all quantification approaches with or without the use of stable isotopes. Blue icons in the boxed area refer to extra steps required when using mass spectrometric signal intensity values for quantification.
Bantscheff et al., Anal Bioanal Chem (2007)
Generic data processing and analysis workflow for quantitative MS

## Slide 23
Exploring quantitative proteomics data using bioinformatics
Kumar et al., FEBS Letters (2009)
Bantscheff et al., Anal Bioanal Chem (2007)

## Slide 24
Protein Quantitation Tool
APEX protein abundance estimate from LC-MS/MS data Java
ASAPRatio (TPP) statistical analysis of protein ratios from ICAT, cICAT, SILAC experiments C++
DAnTE protein quantitation, statistical analysis and visualization .NET, R
isobar quantitation of TMT and iTRAQ data and LaTeX report generation R
IsobariQ quantitation of IPTL, iTRAQ and TMT-labeled peptides C++
Libra (TPP) analyzes 4- and 8-channel iTRAQ data
MaxQuant quantitation from SILAC data from Thermo Orbitrap and FTICR
MFPaQ Mascot file parsing and quantitation using ICAT and SILAC Perl/.NET
MSQuant protein quantitation combining Mascot results and raw data from stable isotope labeling .NET
MS-Spectre quantitiave analysis of multiple LC-MS(/MS) analyses in mzXML Java
Multi-Q tool for multiplexed iTRAQ-based quantitation .NET/Perl
muxQuant multiplexed quantitiave proteomics using differential stable isotope labeling C
PEAKS Q peptide/protein quantification by iTRAQ, ICAT, SILAC or label-free Java
pepXML2Excel converts output from PeptideProphet to protein level information in Excel AWK
ProRata differential proteomics analysis using for various stable isotope labeling schemes
PVIEW isotope labeled, label-free, XIC-based quantitation C++
Quant MATLAB program for protein quantitation by iTRAQ MATLAB
QUIL another program for relative quantitation using stable isotope labeling
RAAMS algorithm for interpreting O-16/O-18 differential proteomics data C++
RelEx calculation of ion current ratios from LC-MS data (requires Xcalibur)
XPRESS (TPP) calculates relative abundances from ICAT, cICAT, SILAC and other N-14/N-15 experiments
Msnbase Base Functions and Classes for MS-based Proteomics R
…

## Slide 25: Absolute quantitation (targeted proteomics)
Selected reaction monitoring (SRM) or multiple reaction monitoring (MRM) is a method of absolute quantitation (also terms AQUA) in targeted proteomics analyses that is performed by spiking complex samples with stable isotope-labeled synthetic peptides that act as internal standards for specific peptides